## Slide 1
Riciclo CO2 e processi chimici sostenibili:
l’esperienza del ricercatore.
Luca Lietti
Incontro ITI Omar, Novara 15.12.21

## Slide 2
OUTLINE
The energy scenario and CO2 emissions
Technologies for CO2 capture and utilization
Research trends in the CO2 utilization
Main players in the field
CONCLUSIONS

## Slide 3
Most of the energy demand is currently satisfied with fossil fuels
The Energy Scenario
Statistical Review of World Energy 2021
© BP p.l.c. 2021
World consumption
Exajoules
Shares of global primary energy
Percentage

## Slide 4
The combustion of fossil fuels emits large amounts of CO2 in the atmosphere
BP Energy Outlook, 2020 Edition
The Energy Scenario
IEA, © 2021

## Slide 5
CO2 concentration in the atmosphere exceeded 415 ppm in April 2020
anthropic CO2 is blamed to be the primary responsible of climate change
  Paul Sudders, National Geographic
  Nature Climate Change 10 (3) cover, 2020
  earthobservatory.nasa.gov/images/hurricane-sandy
Consequences of CO2 emissions

## Slide 6
CO2 emissions: what’s next ?
To reduce CO2 emissions we need to cut the consumption of fossil fuels
We are in the “energy transition” age towards zero- or low-carbon energy sources and vectors

## Slide 7
Reduction of CO2 emissions: CCS and CCU
70% of CO2 is emitted at point source (localized emitters) and can be easily captured
CCS is a treatment of the symptoms but does not eliminate the sources of CO2
CCU uses CO2 as building block, allowing a sustainable carbon cycle strategy

## Slide 8
First step in the CCS and CCU technologies
Technologies are available for the removal of CO2 from flue gases
Direct Air Capture (DAC) is inherently more expensive and requires technological breakthrough to become economically feasible
CO2 capture

## Slide 9
CO2 capture
Direct Air Capture (DAC) is carried out upon adsorption on solid materials

## Slide 10
Reduction of CO2 emissions: CCS

## Slide 11
CO2 is the final product of the combustion of a fossil fuel (transformation of chemical energy into thermal energy)
CO2 is a very stable molecule and is poorly reactive
It is possible to convert CO2 back to fuels, hydrocarbons and chemicals: we need energy or highly reactive molecules (e.g. H2)!
+ heat
Reduction of CO2 emissions: CCU
Chemical conversion

## Slide 12
CO2 hydrogenation allows the production of synthetic fuels (methane, gasoline, diesel fuel) or chemicals (methanol, olefins) with net reduced- or zero-CO2 footprint!
Low-cost renewable H2 (green H2) is necessary for the sustainability of CCU processes
Chemical CO2 utilization
CO2
Fuels
chemicals
H2
Catalytic reactor

## Slide 13
The colors of H2

## Slide 14
H2
Fuels
chemicals
H2O
CO2
Electrolysis
Catalytic reaction
Chemical CO2 utilization

## Slide 15
CO2 to gaseous fuels (SNG)
LCCP
Catalytic reaction carried out over Ru- or Ni-based catalysts
Used also as «storage» of energy (Power-to-gas, power-to-liquids)

## Slide 16
H2
Fuels
chemicals
H2O
CO2
Electrolysis
Catalytic reaction
Chemical CO2 utilization
Catalytic reaction
Key-aspects in research

## Slide 17
CO2 can be transformed (hydrogenated) into fuels (e.g methane, liquid fuels) and chemicals (e.g. methanol, olefins)
To hydrogenate CO2 we need a catalyst!
In these applications, heterogeneous catalysts are used
Research trends in CO2 conversion
  New catalytic materials are required!

## Slide 18
LCCP
Research trends in CO2 conversion
18
  New catalyst formulation

## Slide 19
Catalysts having different shapes and phase loadings can be prepared
Research trends in CO2 conversion

## Slide 20
LCCP
Research trends in CO2 conversion
20
  Catalyst testing
  The catalyst performances can be evaluated

## Slide 21
LCCP
Research trends in CO2 conversion
21
  Mechanistic studies – spectroscopic reactor
simultaneous analysis of surface and gas-phase species
reaction mechanisms can be derived!
Operando FTIR spectrokinetic reactor

## Slide 22
Research trends in CO2 conversion
  Modeling of the catalytic reaction, from the micro- to the macro-scale
  Temperature profiles in the catalyst bed

## Slide 23
catalyst
support
support
adsorbent
adsorbent
catalyst
Adapted from: Kosaka et al., ACS Sustainable Chem. Eng. 2021, 9, 9, 3452–3463
  Based on a cyclic scheme involving CO2 adsorption and hydrogenation (no need of a CO2 separation unit)
  Utilization of Dual Function Materials (DFMs) comprising a CO2 adsorbent and a hydrogenation catalyst:
    Ru for the hydrogenating function
    Alkaline or alkaline earth materials as CO2 adsorbent
Research trends in CO2 conversion
Cyclic CO2 hydrogenation (methanation)

## Slide 24
Research trends in CO2 conversion
  Major players:
  Public research centres (CNR, ENEA), universities (sponsored by private companies, or within the frame of Italian (MITE) and/or European research projects)
  Engineering companies (Tecnimont, Saipem, Wood, …..)
  Energy companies (Eni, …..)
  Other companies (SNAM (distribution), chemical companies, car manufacturers, etc…)

## Slide 25
Research trends in CO2 conversion
  How to participate in a research project:
Apply for an internships in a research center (even before graduation)
Apply for a bachelor and/or master thesis during your career at university
Apply for a research position after graduation (PhD)

## Slide 26
  CCU processes involving captured CO2 and renewable H2 are effective in the production of carbon neutral synthetic fuels and chemicals
  The use of catalytic materials allows the synthesis of selected products (fuels & chemicals)
  Catalysis for CO2 activation is still at the early stages and there is still much work to be done
  Working in this area leads to a great satisfaction and allows you:
  to actively contribute to the resolution of the great problems of the new millennium
  to feel a protagonist in the "man made world" and not a simple spectator
  Zuttel et al., Phil. Trans. R. Soc. A, 2010, 368, 3329 - 3342
CONCLUDING REMARKS

## Slide 27
Thank you for your kind attention!

## Slide 28
Integrated system for chemical CO2 utilization